## Slide 1
https://www.eflm.eu/site/page/a/1194 Version 1.1 / 2018

## Slide 2: Why do we need guidelines?

## Slide 3: Case #1
7:30 a.m.
Patient arrives at the laboratory outpatient unit. His last meal was at 21:00 on the previous day. In the morning he had coffee with milk (without sugar) and one cigarette. Routine chemistry and hematology tests are requested.
Is this patient properly prepared for blood tests?
Yes
No

## Slide 4: Blood collection facts
Most common invasive procedure in the healthcare
Available worldwide (Hospitals, Primary Health Care, Home Based Care)
Huge variations in technique, use of safety devices, disposal methods, reuse of devices and availability of post exposure prophylaxis.
Variations between countries, institutions, individuals
The most common source of preanalytical errors.
Errors often go unrecognized.

## Slide 5
Blood Collection
Sample Transport
Lab Sample handling (Documentation, Centrifugation, Distribution)
Analysis
Result Validation
(Technical, Medical)
Lab Report
Medical Decision
Why to test
(Indication)
What to test (Parameter selection)
Interpretation
Interpretation
Preanalytical
Analytical
Postanalytical
Clinics
Laboratory
Most preanalytical steps occur outside of the laboratory!
Topic of this
presentation
Notes: This slide shows how errors in every single step of the preanalytics may lead to wrong medical decisions
It also shows, that most preanalytical steps occur outside of the laboratory

## Slide 6: Errors within the total laboratory process
Chart: 
| Preanalytical | Analytical | Postanalytical
Verkauf | 61.9 | 15 | 23.1
23 %
62 %
15 %
PREANALYTIC
ANALYTIC
POSTANALYTIC
Lippi G,et al Clin Chem Lab Med 2009; 47:143-153; Carraro P, Plebani M. Clin Chem 2007; 53:1338-1342.
Error rate within the total laboratory process:
0.05% - 10 % of all samples
At what stage in the total laboratory process do these errors occur?

## Slide 7: Consequences of preanalytical errors
  Incorrect test results
  Incorrect diagnosis
  Unnecessary delays
  Harm to the patient and phlebotomist
  Unnecessary cost

## Slide 8: Guidelines
CLSI GP41-A7 Procedures for the Collection of Diagnostic Blood Specimens by Venipuncture
Clinical and Laboratory Standards Institute
WHO guidelines on drawing blood World Health Organization
http://apps.who.int/iris/bitstream/10665/44294/1/9789241599221_eng.pdf
National - Only 7/28 European countries have guidelines
  (Ireland, UK, Spain, Slovenia, Sweden, Italy and Croatia)
  Results from a survey 2013
  Different guidelines and different degrees of compliance
Simundic AM, et al. CCLM 2013;51(8):1585-93.

## Slide 9: Case #2
7:00 a.m.
Patient is lying in his bed. Nurse arrives, asks the patient to sit upright in his bed, and draws one tube of blood. Serum proteins and cholesterol are requested.
Was it correct to ask the patient to sit upright?
  yes
  no

## Slide 10: EFLM RECOMMENDED BLOOD COLLECTION PROCESS
EFLM-Guideline 2016

## Slide 11
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 12
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 13: Workplace preparation
Ensure
patient privacy
continuous workflow
undisturbed access to all necessary supplies.
supplies within expiry date
Materials required
blood collection tubes
needles or winged blood collection sets with safety mechanism
needle holders
tourniquet
gloves
gauze pads, adhesive bandages, or tape
puncture-resistant sharps container
antiseptics: alcoholic and non-alcoholic disinfectants

## Slide 14
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 15: Patient Identification
ID errors are not rare!
  0.1-1% in laboratory medicine
  0.05% in transfusion medicine
Underreported (most go undetected)
Major healthcare issue
Potentially adverse consequences
ZERO TOLERANCE!
Any potentially mislabeled or misidentified specimen
must and will be rejected.
Lippi G, et al. CCLM 2011;49(7):1113–1126

## Slide 16: Patient Identification
At least two independent identifiers:
  Patient full name (the first and the last name )
  Date of birth
Preferably one additional identifier:
  Address
  Health insurance number
  Patient identification number
  ID card details or any other personal identifier
Use open questions: “What is your name?” and “What is your date of birth?”
EFLM WG-PRE – Recommendation on Venous Blood Sampling; CLSI-Guideline GP41-A6

## Slide 17: Patient Identification
If any discrepancies are identified
do not collect samples
until issues are resolved!*
*Exceptions: Unconscious patients, Immigrants without ID number, etc.

## Slide 18
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 19: Patient preparation
Consider:
Has the patient fasted
Has the patient been involved in recent physical activity
Patient positioning
Patient medication / Infusion
Time of day
Test-specific requirements

## Slide 20: Fasting
Blood for all tests should be drawn preferably
in the morning from 7 to 9 a.m. after fasting
(before breakfast / medication)
Simundic AM et al. Clin Chim Acta 2014;432:33-7

## Slide 21: Fasting
Food and liquid (except water)
Alcohol
Smoking
Caffeine
Simundic AM et al. Clin Chim Acta 2014;432:33-7
12 hours
24 hours
Refrain on the day of blood sampling
How long to wait before blood collection
Special Situations: e.g.
Pineapple, Avocado, Banana, Kiwi, Tomato, etc → Serotonin ↑
Protein-rich meals → Homocysteine ↑
Nikolac N et al. Biochem Med 2013;23(3):242-54.

## Slide 22: Fasting
Nordestgaard BG et al.. Eur Heart J 2016.
Parameter | Relative Change 1-6h after standard meal
Triglycerides | 10 – 21%
Total Cholesterol | 1 – 8%
LDL Cholesterol | 4 – 9%
HDL Cholesterol | 0 – 6%

## Slide 23: Fasting
What to do if non-fasting blood collection is impossible?
Document that the patient was not fasting to guide later interpretation.
Kackov, S et al. Biochem Med 2013;23(3):326–31

## Slide 24: Case #1 Result
7:30 a.m.
Patient arrives at the laboratory outpatient unit. His last meal was at 21:00 on the previous day. In the morning he had coffee with milk (without sugar) and one cigarette. Routine chemistry and hematology tests are requested.
Is this patient properly prepared for blood tests?
Yes
No

## Slide 25: Physical activity
Effects of marathon running
Blood collected 1-3 days before and 1 hour after finishing the race
Guder WG, Narayanan S, Wisser H, Zawta B: Diagnostic Samples: From the Patient to the Laboratory, 4th ed.2009 Copyright Wiley-VCH Verlag GmbH & Co. KGaA. Reproduced with permission.
Even moderate exercise (e.g. running to the doctor’s office) can influence laboratory parameters

## Slide 26: What to ask the patient
When was your last meal?
When was your last drink?
What was it?
Have you performed any unusal physical activity in the last 24 hours? („Unusual“ for that specific patient)

## Slide 27: Patient Positioning
Patient should be sitting in a comfortable chair with arms to provide support in case the patient faints
If necessary, patient may lie down
Do not change position before blood sampling!
(if possible)

## Slide 28: Patient Positioning
Guder WG, Narayanan S. Pre-Examination Procedures in Laboratory Diagnostics. 1st ed. DeGruyter, Berlin 2015
Change from supine to upright position
Blood collection preferably after 15 minutes rest in one position

## Slide 29: Case #2
7:00 a.m.
Patient is lying in his bed. Nurse arrives, asks the patient to sit upright in his bed, and draws one tube of blood. Serum proteins and cholesterol are requested.
Was it correct to ask the patient to sit upright?
  yes
  no

## Slide 30: Medication / Infusion
Therapeutic drug monitoring
Always after steady state has been reached
Always document / inform the lab:
WHAT (drug did the patient receive)?
HOW MUCH (of the drug did the patient receive)?
WHEN (was the last intake)?

## Slide 31: Medication / Infusion
Many medications interfere (in-vivo / in-vitro) with laboratory tests.
Examples:
If not avoidable: Blood collection immediately prior to taking the next dose of the drug including information on WHAT? / WHEN? / HOW MUCH?
Nikolac N et al. Biochem Med 2013;23(3):242-54.
Medication | Parameter affected
Anticoagulant therapy | Coagulation testing
Aspirin | Platelet function
Supplements containing iron within the last 10 days | Iron
Insulin | Glucose
Levethyroxine | T4/fT4

## Slide 32: Blood collection using an IV catheter
Whenever possible avoid drawing blood through an
IV catheter.
Catheter collection can impact sample quality through the creation of significantly more hemolysis in samples, sample dilution and contamination of samples
If unavoidable only collect after from a newly inserted catheter, and ideally not after/during infusion, use manual aspiration technique or partial draw blood collection tubes*
*Partial draw tubes are tubes which are designed not be filled completely (e.g. 16x100mm / 4ml)

## Slide 33: Medication / Infusion
Turn off any infusion before blood collection if possible
Blood collection always on the other arm or distal to the infusion site
Recommendation:
Adapted from Guder W et al, Diagnostic Samples: From the Patient to the Laboratory, 4th ed.,Wiley-Blackwell, Weinheim, 2009
Infusion | Earliest time of blood sampling after infusion has been stopped
Lipid | 8 hours
Glucose | 1 hour
Electrolytes | 1 hour
Protein | 1 hour

## Slide 34: Medication / Infusion
Guder WG, Narayanan S, Wisser H, Zawta B: Diagnostic Samples: From the Patient to the Laboratory, 4th ed.2009 Copyright Wiley-VCH Verlag GmbH & Co. KGaA. Reproduced with permission.

## Slide 35: Time of day
Blood for all tests should be drawn preferably
in the morning from 7 to 9 a.m.
(before breakfast / medication)
Simundic AM et al. Clin Chim Acta 2014;432:33-7

## Slide 36: Time of day
Guder WG, Narayanan S, Wisser H, Zawta B: Diagnostic Samples: From the Patient to the Laboratory, 4th ed.2009 Copyright Wiley-VCH Verlag GmbH & Co. KGaA. Reproduced with permission.

## Slide 37
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation
Notes: “Label tubes”: Tube labelling must be done in presence of the patient. Labelling before or after blood collection should be based on a prospective risk analysis of the phlebotomy process in each institution.

## Slide 38: Label tubes
Tube labelling or tube cross-identification must be done in the presence of the patient. Labelling before or after blood collection should be based on a prospective risk analysis of the blood collection process in each institution.
Tube information should at least contain:
    Patient first and last name
    Date of birth
    ID number
    Preferable additional information on the tube:
    Date
    Time (if necessary, e.g. for TDM)
    ID of the phlebotomist
    (or there should be a mechanism to identify a phlebotomist)
If this information is not printed directly on the label, a mechanism must be in place to identify this information for example through IT systems (e.g. laboratory/hospital information systems)
EFLM WG-PRE – Recommendation on Venous Blood Sampling; CLSI-Guideline GP41-A6

## Slide 39: Label tubes
Visible fill line
Labelled straight vertically
Labelled high
Labelled all around
(Fill line not visible)
Labelled too low
Labelled askew
Labelled horizontally
X
X
X
X

## Slide 40: Label tubes
Avoid contact of the label with disinfectant
+
=

## Slide 41
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation
Notes: „sanitize hands“: Cleaning of hands in front of patients is also important in reassuring a patient, but is not necessary if gloves are worn.

## Slide 42: Put on gloves / Sanitize hands
Cleaning of hands in front of patients is also important in reassuring a patient.
To minimize blood stasis it is recommended putting on gloves prior to tourniquet application.
Always use a new pair of gloves for each patient.
Lima-Oliveira G, et al. Biochemia Medica 2012;22(3):342-51.

## Slide 43
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 44: Apply tourniquet
Apply tourniquet only if necessary.
EFLM-recommendation: Collect blood without tourniquet whenever possible.
Try to minimize the use of a tourniquet for the following collections:
  lactate
  ammonia
  albumin
  calcium
Tourniquets are a source of MRSA
(Through poor hand hygiene. Therefore use single-use devices!)

## Slide 45: Apply tourniquet
When using a tourniquet:
7 - 10 cm (4–5 finger width) proximal to the puncture site
Release ≤ 1 minute (If > 1 minute, release and reapply after 2 min)
Pumping (fist clenching) should not be done!

## Slide 46: Apply tourniquet
Fist clenching leads to an increase in potassium !!
Don BR et al. N Engl J Med 1990;322(18):1290-2.

## Slide 47: Release Tourniquet
As soon as possible after the
blood begins to flow into tube

## Slide 48: Helpful tools
Vein illumination device
for better vizualisation of the veins
Vein Viewer® Flex – Greiner BioOne

## Slide 49
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 50: Select a puncture site
Putz R and Pabst R eds. Sobotta: Atlas of Human Anatomy. 20th ed. Munich, DE: Urban & Schwarzenberg/Elsevier, 1993.
Reprinted with kind permission of the Elsevier GmbH
  Do not collect blood from:
  previously placed peripheral venous catheters
  indurated veins
  paretic arm
  arms with lymphatic drain disorders
Selecting the best vein for venipuncture is important:
  sample quality,
  patient satisfaction,
  to avoid nerve damage,
  to avoid arterial puncture,
  ease and speed of collection

## Slide 51
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 52: Clean sampling site
CLSI GP41-A7 guideline recommends that the puncture site must be cleaned to prevent contamination of a patient or a sample
Use 70% ethyl alcohol
For blood culture collection let alcohol dry for a minimum of 60 seconds
When collecting a sample for alcohol concentration measurements, the use a non-alcoholic disinfectant is preferable.
Clean site with on wipe and let it dry.
To prevent hemolysis
To prevent patient experiencing a burning sensation during puncture
To allow the alcohol to sterilise the puncture site
Salvagno GL et al. Biochem Med 2013;23(2):201-5.
Failure to let alcohol dry is not associated with sample hemolysis !
Lippi G et al. Biochem Med 2017; 27(2):398-403

## Slide 53
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 54: Puncture the vein - Vacuum System
1 Ensure appropriate conditions and supplies
required for phlebotomy
2 Label and/or identify tubes
3 Clean hands in front of the patient
4 Put on gloves
5 Assemble appliances
6 Apply tourniquet
7 Select venepuncture site
8 Clean sampling site
9 Puncture the vein
10 Draw first tube
11 Release the tourniquet as soon as the
blood flows into the first tube
12 Gently invert the tubes 1 time
immediately after collection
13 Draw additional tubes following order of draw
14 Remove needle from the vein
15 Activate safety mechanism
16 Dispose of the needle
17 Ensure the bleeding has stopped
18 Treat the puncture wound
19 Tell a patient to apply a pressure on the wound
20 Invert all tubes 4 times
21 Remove gloves
22 Clean hands

## Slide 55: Puncture the vein - Aspiration System
1 Ensure appropriate conditions and supplies
required for phlebotomy
2 Label and/or identify tubes
3 Clean hands in front of the patient
4 Put on gloves
5 Assemble appliances
6 Apply tourniquet
7 Select venepuncture site
8 Clean sampling site
9 Puncture the vein
10 Draw first tube
11 Release the tourniquet as soon as the
blood flows into the first tube
12 Gently invert the tubes 1 time
immediately after collection
13 Draw additional tubes following order of draw
14 Remove needle from the vein
15 Activate safety mechanism
16 Dispose of the needle
17 Ensure the bleeding has stopped
18 Treat the puncture wound
19 Tell a patient to apply a pressure on the wound
20 Invert all tubes 4 times
21 Remove gloves
22 Clean hands

## Slide 56: Puncture the vein
Puncture the vein with the bevel up, as it minimizes the pain and reduces the risk of perforation of the back wall of the vein
If the first blood collection attempt is unsuccessful, the second attempt should be made on the other arm.
If a third attempt should be necessary, it should be performed distal to the previous puncture sites. Also consider calling a more experienced colleague.

## Slide 57: Helpful tools
Sharps device with flash visualisation
Needle & wingsets are available that either through design or as part of the method of operation that will provide a visible flash indication when the needle has penetrated the vein
Image: With kind permission from Becton Dickinson ©

## Slide 58: Blood borne pathogens
Possible transmission of a variety of pathogens including HIV, Hepatitis B + C, and other
Use medical devices incorporating a safety-engineered protection mechanism
Place effective disposal procedures and clearly marked and technically safe sharps containers
Use Personal Protective Equipment (Gloves)
NEVER recap a used needle

## Slide 59
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 60: Case #3
Nurse needs to draw EDTA, serum and citrate tubes from a patient. Which is the correct order of draw?
Coagulation (citrate) > EDTA > Serum
EDTA > Coagulation (citrate) > Serum
Coagulation (citrate) > Serum > EDTA
The order of draw does not matter. It is not important.

## Slide 61: Order of draw
Important to:
assure sample quality
avoid cross-contamination of additives between tubes
Evidence shows that it occurs and may affect the quality of results
Cornes MP et al. Clin Chem Lab Med 2013; 51:e285 - e285.

## Slide 62: Order of draw
Coagulation tube as first tube?
When using a winged safety blood collection set, a discard tube must be used to prevent underfilling.
No discard tube is needed when
straight needles are used for
blood collection.
EFLM-Guideline on Venous blood collection; CLSI H21-A5 ; CLSI GP41-A6
Image with kind permission of Greiner Bio-One©

## Slide 63: Order of draw
EFLM WG-PRE Recommendation
In agreement with ISO 6710:1995 Preview
Single-use containers for venous blood specimen collection
Cap colors in your hospital might differ, please refer to your laboratory
Blood culture |  | 
Citrate tube |  | ESR*
Serum tube with or without barrier |  | 
Heparin tubes with or without barrier |  | 
EDTA tubes |  | 
Glucose tubes |  | 
Other tubes (e.g. trace elements) |  | 
*Erythrocyte sedimentation rate

## Slide 64: Case #3
Nurse needs to draw EDTA, serum and citrate tubes from a patient. Which is the correct order of draw?
Coagulation (citrate) > EDTA > Serum
EDTA > Coagulation (citrate) > Serum
Coagulation (citrate) > Serum > EDTA
The order of draw does not matter. It is not important.

## Slide 65: Tube filling
Consequence of underfilled coagulation tube:
Too much citrate per ml blood
→ Incorrect coagulation results
Even slightly underfilled tubes may lead to erroneous coagulation results
Minimum
Maximum
Images with kind permission of Becton Dickinson © , GBO © , Sarstedt ©
Minimum

## Slide 66: Tube filling
Never transfer blood from a syringe or another blood collection tube !!!!

## Slide 67
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 68: Remove needle from the vein
After disconnecting the last tube place a gauze on the venipuncture area, without applying pressure.
Gently remove the needle and immediately activate the safety mechanism
Apply pressure to the puncture site with the gauze to prevent bleeding

## Slide 69: Activate Safety Device and dispose needle
Aspiration
system
Evacuated blood collection
system
Butterfly
Images with kind permission of Sarstedt and Greiner Bio-One©

## Slide 70
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 71: Bandage puncture site and advise Patient
Check that the bleeding has stopped. Apply an adhesive bandage securely over a dry pad/gauze square.
Ask the patient to apply pressure for at least 2 minutes for routine draws and up to 10 minutes for patients on anticoagulation.
If cephalic basilic vein is used, ask the patient not to bend the arm

## Slide 72
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 73: Invert tubes
Blood must be mixed with anticoagulant
Invert tubes gently 1x directly after collection and
4x after collection of all tubes
If only one tube is collected, invert 5 x directly after collection.
No mixing → Risk of clotted sample and latent clotting in serum samples
Do NOT shake the sample → sample hemolysis !

## Slide 74: Sample hemolysis
Lippi G, et al. Clin Chem Lab Med 2008; 46:764-772.

## Slide 75: Sample hemolysis
Consequences
Interference with chromatic measurements
Release of intracellular components after erythrocyte rupture
Lippi G, et al. Clin Chem Lab Med 2008; 46:764-772.

## Slide 76
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 77: Remove gloves
Always remove gloves by turning them inside out.
Before removing the second glove place the first one in your fist.
Thereby you should have one bundle with all potentially infectious substances facing inwards.

## Slide 78
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 79: Advise patient to rest
Advise patient to rest for 5 minutes and ensure bleeding has stopped before leaving the area where blood collection took place

## Slide 80
Pre-Sampling
Sampling
Post-Sampling
Patient identification
Patient preparation
Label tubes*
Communication
Workplace preparation
Test request
Assemble supplies
(Sanitize hands)
Release tourniquet
Draw first tube
Puncture the vein
Clean sampling site
Select puncture site
Apply tourniquet
Put on gloves
Gently invert tubes
Draw tubes in order
Remove needle
Dispose of needle
Bandage puncture site
Invert all tubes
Remove gloves
Advise patient
(Label tubes)*
Advise patient to rest
Transport the sample
* Depending on local risk assesment – see respective slide in this presentation

## Slide 81: Sample transportation
The laboratory should be asked for advice on proper transport conditions.
You are in charge of the prompt and proper transportation of the samples you collected.
Nikolac N et al. Biochem Med 2013;23(3):242-54.

## Slide 82
The quality of laboratory analyses depends to a large degree on correct preanalytical blood collection practices and sample handling for which you are responsible.
Deviation from the proposed Guideline might lead to false laboratory reports and potentially harms the patient!
Contact your laboratory if you are in any doubt or if you have any questions.

## Slide 83
For more information (knowledge test, observation sheet, videos, …) visit the website of the
EFLM Working Group „Preanalytical Phase“
https://www.eflm.eu/site/page/a/1156